## Slide 1: Overview of Physical Storage Media

## Slide 2
Several types of data storage exist in most computer systems. These storage media are classified by the speed with which data can be accessed, by the cost per unit of data to buy the medium, and by the medium’s reliability. Among the media typically available are these:
Cache:-
The cache is the fastest and most costly form of storage.
Cache memory is small; its use is managed by the computer system hardware.
We shall not be concerned about managing cache storage in the database system.

## Slide 3
Main memory:-
The storage medium used for data that are available to be operated on is main memory.
The general-purpose machine instructions operate on main memory.
Although main memory may contain many megabytes of data, or even gigabytes of data in large server systems, it is generally too small (or too expensive) for storing the entire database.
The contents of main memory are usually lost if a power failure or system crash occurs.

## Slide 4
Flash memory:-
Also known as electrically erasable programmable read-only memory (EEPROM), flash memory differs from main memory in that data survive power failure.
Reading data from flash memory takes less than 100 nanoseconds (a nanosecond is 1/1000 of a microsecond), which is roughly as fast as reading data from main memory.
However, writing data to flash memory is more complicated—data can be written once, which takes about 4 to 10 microseconds, but cannot be overwritten directly.
To overwrite memory that has been written already, we have to erase an entire bank of memory at once; it is then ready to be written again.
A drawback of flash memory is that it can support only a limited number of erase cycles, ranging from 10,000 to 1 million.
Flash memory has found popularity as a replacement for magnetic disks for storing small volumes of data (5 to 10 megabytes) in low-cost computer systems, such as computer systems that are embedded in other devices, in hand-held computers, and in other digital electronic devices such as digital cameras.

## Slide 5
Magnetic-disk storage:-
The primary medium for the long-term on-line storage of data is the magnetic disk. Usually, the entire database is stored on magnetic disk.
The system must move the data from disk to main memory so that they can be accessed.
After the system has performed the designated operations, the data that have been modified must be written to disk.
The size of magnetic disks currently ranges from a few gigabytes to 80 gigabytes.
Both the lower and upper end of this range have been growing at about 50 percent per year, and we can expect much larger capacity disks every year.
Disk storage survives power failures and system crashes.
Disk-storage devices themselves may sometimes fail and thus destroy data, but such failures usually occur much less frequently than do system crashes.

## Slide 6
Optical storage :-
The most popular forms of optical storage are the compact disk (CD), which can hold about 640 megabytes of data, and the digital video disk (DVD) which can hold 4.7 or 8.5 gigabytes of data per side of the disk (or up to 17 gigabytes on a two-sided disk).
Data are stored optically on a disk, and are read by a laser.
The optical disks used in read-only compact disks (CD-ROM) or read-only digital video disk (DVD-ROM) cannot be written, but are supplied with data prerecorded.
There are “record-once” versions of compact disk (called CD-R) and digital video disk (called DVD-R), which can be written only once; such disks are also called write-once, read-many (WORM) disks.

## Slide 7
There are also “multiple-write” versions of compact disk (called CD-RW) and digital video disk (DVD-RW and DVD-RAM), which can be written multiple times.
Recordable compact disks are magnetic–optical storage devices that use optical means to read magnetically encoded data.
Such disks are useful for archival storage of data as well as distribution of data.

## Slide 8
Tape storage:-
Tape storage is used primarily for backup and archival data. Although magnetic tape is much cheaper than disks, access to data is much slower, because the tape must be accessed sequentially from the beginning.
For this reason, tape storage is referred to as sequential-access storage. In contrast, disk storage is referred to as direct-access storage because it is possible to read data from any location on disk.
Tapes have a high capacity (40 gigabyte to 300 gigabytes tapes are currently available), and can be removed from the tape drive, so they are well suited to cheap archival storage.
Tape jukeboxes are used to hold exceptionally large collections of data, such as remote-sensing data from satellites, which could include as much as hundreds of terabytes (1 terabyte = 1012 bytes), or even a petabyte (1 petabyte = 1015 bytes) of data.